## Slide 1
FOSS4G WORKSHOP
From a tiny Thing to geospatial data on the web
An Arduino/XIAO ESP32-C3 path through sensors, GNSS, Wi-Fi, GeoJSON, and HTTP POST.
Step1 -> Step7 repo flow
Editable deck generated from the current repository materials

## Slide 2
WORKSHOP MAP
Seven repo steps, one data pipeline
The step numbers on the slides match the current repository folders and sketches.
Step1
Setup
Step2
Log
Step3
Sensor
Step4
GNSS
Step5
Wi-Fi
Step6
GeoJSON
Step7
POST
Teaching move
Every step adds one capability to the same Thing.
Participant rhythm
Upload, observe Serial Monitor, debug one thing, then move forward.
FOSS4G lens
End with interoperable geospatial data that another service can consume.
iot-xiao-cursus / overview
FOSS4G workshop

## Slide 3
ARCHITECTURE
A tiny field device becomes a geospatial publisher
The technical shape is deliberately small, standards-friendly, and inspectable.
Sensor
value
XIAO
ESP32-C3
GNSS
WGS 84
Wi-Fi
network
GeoJSON
Feature
HTTP POST -> backend / measurements
{
"type": "Feature",
"geometry": { "type": "Point" },
"properties": { "value": 21.5 }
}
No hidden cloud magic
Serial output makes each layer visible
GeoJSON keeps the location model portable
iot-xiao-cursus / architecture
FOSS4G workshop

## Slide 4
STEP1_SETUP
Prepare the board and the mental model
Arduino IDE, XIAO ESP32-C3, setup()/loop(), and the first upload.
Hardware target
Seeed Studio XIAO ESP32-C3: 3.3V I/O, Wi-Fi + Bluetooth, compact enough for workshop tables.
IDE setup
Install Arduino IDE, add ESP32 board support, select XIAO_ESP32C3 and the USB serial port.
Programming model
Participants see the Arduino abstraction: setup() once, loop() forever.
void setup() {
pinMode(LED_NOTBUILTIN, OUTPUT);
}
void loop() {
digitalWrite(LED_NOTBUILTIN, HIGH);
delay(1000);
}
iot-xiao-cursus / Step1
FOSS4G workshop

## Slide 5
STEP2_LOG
Make the invisible board speak
Serial Monitor becomes the workshop microscope.
Serial.begin(115200);
uint64_t chipid = ESP.getEfuseMac();
Serial.println(mac2String((byte*)&chipid));
Open Tools > Serial Monitor
Confirm baud rate: 115200
Read the unique MAC address
Match the last bytes to the sticker on the board
Why it matters
Device identity is the first bridge from hardware to data infrastructure. Each Thing needs a stable way to be recognized.
Teaching cue
When participants see text from the board, the loop between code, hardware, and observation clicks.
iot-xiao-cursus / Step2
FOSS4G workshop

## Slide 6
STEP3_SENSOR
Attach reality to the Thing
A sensor adds the first measurement value, but wiring discipline comes first.
Safety first
Disconnect USB before wiring. Never connect 5V directly to GND.
Breadboard basics
Use jumpers for VCC and GND. Use signal wires for the sensor protocol.
Protocol choices
The course can use analog voltage, digital signals, or I2C sensors.
// Choose one sensor header
#include "../sensors/AM-2320.h"
// #include "../sensors/dummy_sensor.h"
float temperature = getTemperature();
float humidity = getHumidity();
iot-xiao-cursus / Step3
FOSS4G workshop

## Slide 7
STEP4_GNSS
Turn a sensor node into a location-aware Thing
The GNSS module returns WGS 84 latitude and longitude when it has a valid fix.
GNSS VCC -> XIAO 5V
GNSS GND -> XIAO GND
GNSS TX -> XIAO D7 / RX
Fix: yes
Status: valid GNSS fix
Latitude: 52.110352
Longitude: 4.897106
Core idea
TX sends, RX receives. The GNSS module talks; the XIAO listens.
Debug signal
Chars processed tells you whether serial data arrives. Fix: yes tells you whether coordinates are valid.
GeoJSON preview
Later, GeoJSON will use [longitude, latitude], not the conversational latitude/longitude order.
iot-xiao-cursus / Step4
FOSS4G workshop

## Slide 8
STEP5_WIFI
Give the Thing a network path
The ESP32-C3 Wi-Fi stack turns local measurements into connected measurements.
#pragma once
#define SECRET_SSID "iot-workshop"
#define SECRET_PASS "********"
[WiFi] Connected
[WiFi] IP address : 192.168.1.113
[WiFi] Signal strength : -42 dBm
Keep credentials out of Git
Use 2.4 GHz networks for compatibility
Scan nearby SSIDs when debugging
Print status, IP, gateway, DNS, and RSSI
iot-xiao-cursus / Step5
FOSS4G workshop

## Slide 9
STEP6_GEOJSON
Assemble an interoperable measurement
Sensor + GNSS + Wi-Fi status becomes one GeoJSON Feature.
GeoJsonMeasurement measurement = getCurrentMeasurement();
String geoJson = buildGeoJson(measurement);
Serial.println(geoJson);
{
"type": "Feature",
"geometry": {
"type": "Point",
"coordinates": [4.897106, 52.110352]
},
"properties": { "value": 21.5, "unit": "C" }
}
Design choice
The .ino shows where data comes from; helpers own reusable formatting and device services.
No fix?
Use geometry: null while still reporting sensor and debug properties.
iot-xiao-cursus / Step6
FOSS4G workshop

## Slide 10
STEP7_REQUEST
Send the GeoJSON to a backend
HTTP POST is the handoff from workshop device to web service.
const char* BACKEND_URL =
"http://192.168.0.100:8000/measurements";
Content-Type: application/geo+json
Do not use localhost on the XIAO
Use the laptop IP on the same Wi-Fi network
Docker backend must publish 8000:8000
Backend should listen on 0.0.0.0
GeoJSON
body
HTTP
POST
Backend
/measurements
iot-xiao-cursus / Step7
FOSS4G workshop

## Slide 11
DEBUGGING MODEL
Use the Serial Monitor as a layered health check
Each step introduces one new failure surface and one new diagnostic signal.
Board
Selected XIAO_ESP32C3, correct COM port, upload succeeds
Serial
115200 baud, MAC address prints
Sensor
Value is not null; wiring and library match the active header
GNSS
Chars processed increases; Fix becomes yes outdoors or near a window
Wi-Fi
SSID found, IP assigned, RSSI reasonable
Backend
POST target uses laptop IP, Docker port is published
iot-xiao-cursus / debug
FOSS4G workshop

## Slide 12
WHY THIS BELONGS AT FOSS4G
Small hardware, open standards, visible data
The workshop makes geospatial interoperability tangible at table scale.
Open formats
GeoJSON makes the measurement inspectable and easy to pass between tools.
Real coordinates
GNSS outputs WGS 84 positions and introduces the longitude/latitude convention.
Web-native delivery
HTTP POST connects field observations to ordinary web backends and APIs.
Teaching standards
Participants can see why SensorThings-style thinking separates Things, Sensors, Observed Properties, and Locations.
iot-xiao-cursus / FOSS4G
FOSS4G workshop

## Slide 13
FACILITATION TIMING
A practical rhythm for a live session
Keep each step observable before moving to the next capability.
Step1 20 min
IDE, board, first upload
Step2 10 min
Serial Monitor + MAC
Step3 25 min
sensor wiring and values
Step4 25 min
GNSS and valid fix
Step5 15 min
Wi-Fi diagnostics
Step6 20 min
GeoJSON Feature
Step7 20 min
POST to backend
Reserve extra time for USB cables, serial ports, and first GNSS fixes.
iot-xiao-cursus / facilitation
FOSS4G workshop

## Slide 14
REPO MAP AND SOURCES
Use the deck alongside the repository
Slide titles intentionally mirror the current folder names.
Step1_Setup: board, IDE, programming, Blink
Step2_Log: Serial Monitor and MAC address
Step3_Sensor: wiring and sensor values
Step4_GNSS: WGS 84 coordinates and fix status
Step5_WiFi: credentials, network status, RSSI
Step6_GeoJSON: GeoJSON Feature builder
Step7_request: HTTP POST body and backend URL
Primary sources
Local repository README files, current Step folders, sketches, helpers, and components list. No external visual assets used.
Presenter note
Use this deck as the narrative spine. Use the repo for live uploads, serial output, and hands-on fixes.
iot-xiao-cursus / sources
FOSS4G workshop